## Slide 1
SPC Machine Learning
ANALYSIS
1590nm Amp Test · Yield · CONQ · Failure Prediction
Dean Foulds
Data Scientist & ML Engineer | ASN Submarine Cables
deanfoulds.xyz
Key Stats
99.7%
Process Yield
21,420
Total Tests 2023
1,601
Out-of-Control
143K GBP
CONQ

## Slide 2
Study Overview
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
Can machine learning accurately predict failures from SPC analysis of 1590nm electrical amp testing?
Problem
No real-time data feedback from splicing machines
Blind splicing drives high CONQ
1,601 / 21,420 tests out-of-control (7.5%)
Reactive quality model
Approach
SPC charting on full 2023 dataset
Z-score outlier removal at 2.7 sigma
Lazy Regressor benchmark: 40+ models
XGBoost & SVR selected as final models
Outcome
99.7% splice yield confirmed
Amp-stage test captures 13% failures early
SVR predicts amp values with low MSE
CONQ reduction roadmap established

## Slide 3
Causes of Amp Splice Failures
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
Pulled Fibre
Mechanical stress during assembly causing fibre extraction from the splice point
Tight Fibre
Insufficient slack leading to tension-induced breaks under thermal or mechanical load
Poor Routing
Incorrect cable path creating excessive bend radius and stress concentration points
Foam Pressure
External compression from protective foam causing gradual signal degradation
Too Many Fibres
Overcrowding at the splice point causing physical interference between fibres
Manufacturing Deviations
Process deviations during production — root cause of C1 failures (26.7% of all failures)

## Slide 4
Yield Calculation & Cost of Non-Quality
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
Process Yield
99.7%
(94,432 - 318) / 94,432 x 100 = 99.7%
(Splices - Failures) / Splices x 100
2,951
Amps Produced
32
Splices/Unit
318
Failures
C1 failures = 85 / 318 = 26.7% of all splice failures
Cost of Non-Quality (CONQ)
143,135
GBP
N x (T x P x C_labour + C_material + C_overhead)
N=318
Rework
T=3h
Per rework
P=3
Persons
50 GBP/h
Labour
20 GBP
Material
15 GBP
Overhead
318 x (3 x 3 x 50 + 20 + 15) = 318 x 450 = 143,100 GBP

## Slide 5
SPC Results — All Amp Tests (1590nm)
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
SPC chart for all 2023 1590nm amp tests. Out-of-control points highlighted. UCL=43, LCL=39. Total: 21,420 tests, 1,601 out-of-control (7.5%).

## Slide 6
Visualising Out-of-Control Points
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
Scatter overlay showing out-of-control points against the SPC line chart. Serial numbers of failed units identified for traceability.

## Slide 7
Distribution Analysis — Results
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
Histogram with normal distribution curve fitted. Z-score lines at 2 and 3 sigma shown in green. Data exhibits near-normal distribution post-cleaning.

## Slide 8
Outliers Removed — Box Plot
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
Box plot after Z-score outlier removal at threshold 2.7 sigma. Distribution tightened significantly, reducing noise for ML model training.

## Slide 9
SPC Analysis — Majority Outliers Removed
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
SPC chart after outlier removal. Remaining out-of-control points represent true systematic failures. Much cleaner signal for predictive modelling.

## Slide 10
Logistic Regression Analysis — Pass/Fail vs Results
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
Scatter plot of Results vs Test Status (0=FAIL, 1=PASS) with OLS trendline. Shows correlation between measurement values and pass/fail outcomes.

## Slide 11
Pass/Fail Criteria — Label Encoding
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
Test Status encoded as binary labels: FAIL=0, PASS=1. Used as feature alongside Limit High Flt and Limit Low Flt for model training.

## Slide 12
Initial Lazy Regressor Results — Model Benchmarking
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
Automated benchmarking of 40+ sklearn models. Ranked by R-squared, RMSE and adjusted R-squared. XGBoost and SVR identified as top performers.

## Slide 13
XGBoost Predictions vs Actual SPC Results
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
XGBoost (n_estimators=400, lr=0.08, max_depth=3) predictions (purple dots) overlaid on actual results (blue line). Control limits shown in red.

## Slide 14
XGBoost Predictions — Zoomed View
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
Zoomed view of XGBoost predictions vs actual values. Model tracks the SPC curve closely within control limits, demonstrating strong predictive accuracy.

## Slide 15
SVR (RBF Kernel) Predictions vs Actual
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
Support Vector Regression predictions overlaid on actual SPC results. SVR achieved lowest test MSE of 0.0048 — selected as production model.

## Slide 16
SVR Predictions — Zoomed View
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
Zoomed SVR prediction view. Tight clustering of predictions around actual values confirms model accuracy within the UCL/LCL control window.

## Slide 17
First Prediction — Known Input Validation
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
Validation: Input [41.523, 41.723, 0] -> SVR Predicted: 42.044. Green dot shows new test point plotted against historical SPC data. Within UCL.

## Slide 18
Machine Learning Models — Evaluation & Selection
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
Decision Tree
Baseline
Initial baseline. Fast, interpretable. Established benchmark R-squared score for comparison.
- 80/20 split, random_state=42
- Target: Results (continuous)
- Benchmark for all other models
Lazy Regressor
Screening
Benchmarked 40+ sklearn models automatically. Identified XGBoost & SVR as top performers without manual tuning.
- 40+ models ranked by R-sq & RMSE
- No hyperparameter tuning required
- Fast automated candidate selection
XGBoost
Primary Model
n_estimators=400, max_depth=3, lr=0.08. Gradient boosted trees trained on UCL/LCL boundary labels.
- subsample=0.8, colsample_bytree=0.8
- eval_metric: RMSE
- Saved: amps.model
SVR (RBF Kernel)
Production
Best test MSE=0.0048. Non-linear RBF kernel. Final deployed model for real-time prediction.
- kernel='rbf' (non-linear)
- Input [41.523,41.723,0] -> 42.044
- Saved: svr_model.pkl
Features: Limit High Flt, Limit Low Flt, Test Status | Target: Results | SVR selected as production model

## Slide 19
Conclusions & Recommendations
Dean Foulds | SPC Machine Learning Analysis | ASN Submarine Cables
99.7% Yield
Highly efficient splice process across 94,432 total splices. C1 failures at 26.7% require targeted root cause analysis.
CONQ = 143K GBP
Cost of non-quality driven by blind splicing. Real-time data feedback would eliminate the majority of rework costs.
7.5% Out-of-Control
1,601 from 21,420 2023 tests outside UCL/LCL. Amp-stage test captures 13% early, enabling proactive intervention.
SVR Best Model
SVR with RBF kernel achieved lowest test MSE of 0.0048. Successfully predicts amp measurements from control inputs.
Data Feedback Gap
Lack of real-time data from splicing machines directly proportional to CONQ increase — highest priority recommendation.
Next Steps
Deploy SVR with live SPC monitoring. Investigate C1 root cause. Automate alerts when predictions approach UCL/LCL.

## Slide 20
Thank You
Dean Foulds
Data Scientist & ML Engineer
deanfoulds.xyz | github.com/Dean-Foulds | LinkedIn: dean-foulds
94,432
Splices Analysed
99.7%
Process Yield
4 Models
Evaluated
143K GBP
CONQ Identified